## Slide 1: Highly available, causally ordered group chat
Francesco Spangaro – Giacomo Orsenigo – Federico Saccani

## Slide 2
Peer to peer connection with a discovery server
Using Java UDP sockets
Acks to detect network failures
Network: Implementation choices
Discovery Server
Peer1
Peer2
Peer3
Peer4

## Slide 3
Peers are reliable, they can join and leave the network at any time
The discovery server is always reachable by all peers
Network failures and partitions can happen
Network: Implementation assumptions
Discovery Server
Peer1
Peer2
Peer3
Peer4

## Slide 4: Peer's Connection Setup
The new peer asks the discovery server for the list of addresses.
Map<user, address>
The new peer try to contact all other peers, sending an HelloPacket.
Peers
A: <addr>
B: <addr>
C: <addr>
Peers
A: <addr>
B: <addr>
C: <addr>
D: <addr>
Notes: La connessione di un nuovo peer avviene in 2 fasi:
Il nuovo peer invia al discovery un pacchetto contenente il suo nome e la porta sulla quale ascolterà per nuove connessioni. Il discovery server risponde con l’elenco di tutti i peer attivi e i relativi indirizzi.
A questo punto il nuovo peer invia a loro un pacchetto contenente il suo nome. Se ricevono l’ack la connessione è stabilita, altrimenti il peer viene segnato come non raggiungibile e verranno fatti nuovi tentativi più avanti.
A questo punto è possibile procedere con la creazione di una nuova chat.

## Slide 5: Peer's Connection (code)
private void connectToSinglePeer(String id, SocketAddress addr) throws IOException { LOGGER.info(STR."[\{this.id}] connecting to \{id}: \{addr}"); socketManager.send(new HelloPacket(this.id), addr); onPeerConnected(id, addr); }
private void onPeerConnected(String id, SocketAddress addr) { LOGGER.info(STR."[\{this.id}] \{id} connected"); ips.put(id, addr); unreachablePeers.remove(id); if (!connectedPeers.contains(id)) { connectedPeers.add(id); controller.resendQueued(id); usersPropertyChangeSupport.firePropertyChange("USER_CONNECTED", null, id); } }
Send an HelloPacket containing my username
This is called both when we are connecting to a new peer or a new peer is connecting to us.
Update users’ list on GUI
Save the address of the new peer
Resend enqueued packets (if any)

## Slide 6
A
B
C
Chat name
Set<User>
Chat name
Set<User>
Chat name:
<empty>
Chat name:
<empty>
Chat name:
<empty>
Chat Creation

## Slide 7
A
B
C
Message 1
Chat 1
Message 1
Chat 1
Chat 1:
Message 1
Chat 1:
Message 1
Chat 1:
Message 1
Sending a message (without network faults)

## Slide 8: Network faults
All packets are acknowledged to detect network faults
All packets sent during faults are enqueued
Automatically retry to reconnect
When reconnected, send enqueued packets
A
B
C
Notes: Se dopo aver inviato un pacchetto non viene ricevuto l’ack di conferma, il peer corrispondente viene considerato disconnesso.
Tutti i pacchetti da inviare al peer disconnesso vengono accodati.
A intervalli regolari, ogni peer cerca di riconnettersi a tutti i peer attualmente non connessi.
In caso di esito positivo, vengono inviati tutti i pacchetti che nel frattempo erano stati accodati.
In questo modo i peer connessi potranno continuare a comunicare e, quando la connessione tornerà attiva, il peer disconnesso riceverà tutti i messaggi.

## Slide 9: Vector clocks for causal delivery
Order between messages and replies is preserved
Increment personal clock only when sending a message
On message reception check the clocks
Hold a message until all previous messages are received:
  ts(r)[j] = Vk[j]+1
  ts(r)[i] ≤ Vk[i] ∀ i ≠ j
If there are no previous messages accept the message and merge the clocks

## Slide 10: Sending a message (network faults)
A
B
C
Message 1
Chat 1
Message 1
Chat 1
Chat 1:
Message 1
Chat 1:
Message 1
Resend queue:
B -> Message 1 (chat 1)
Chat 1:
<Empty>

## Slide 11: Sending a message (network faults)
A
B
C
Chat 1:
Message 1
Chat 1:
Message 1
Resend queue:
B -> Message 1 (chat 1)
Message 2
Chat 1
Message 2
Chat 1
Chat 1:
<Empty>
Notes: C risponde.
A e C continuano a comunicare normalmente, mentre B non può accettare i nuovi messaggi.

## Slide 12: Sending a message (network faults)
A
B
C
Chat 1:
Message 1
Message 2
Chat 1:
Message 1
Message 2
Resend queue:
B -> Message 1 (chat 1)
Message 1
Chat 1
Enqueued messages:
Message 2 (chat 1)
When the network recovers
All messages are received in correct order
Chat 1:
Message 1
Message 2
Chat 1:
<Empty>
Notes: Quando la connessione viene ristabilita, viene nuovamente inviato il pacchetto iniziale (contenente user e porta), che in questa slide è stato omesso.

## Slide 13: Creating a message (code)
public Message createLocalMessage(String msg, String sender) { try { pushLock.lock(); vectorClocks.put(sender, vectorClocks.get(sender) + 1); Message m = new StringMessage(msg, Map.copyOf(vectorClocks), sender); receivedMsgs.add(m); propertyChangeSupport.firePropertyChange( … ); return m; } finally { pushLock.unlock(); } }
Only one message at the time can be add to a chat
Increment the sender's clock
Create the message with updated clocks
Update GUI
Then the message is sent to all the peers in the chat

## Slide 14: Checking vector clocks on reception (code)
private int checkVC(Message m) { Map<String, Integer> newClocks = Map.copyOf(m.vectorClocks()); boolean senderFound = false; for (String u : users) { if (newClocks.get(u) == vectorClocks.get(u) + 1 && !senderFound){ senderFound = true; } else if ((newClocks.get(u) > vectorClocks.get(u))) { return -1; } } if (!senderFound) return 0;
return 1; }
Check if one entry in the vector clock map has increased
The first entry that is increased by 1, we assume it's the sender
If no clocks incremented, drop the message
If any other entry has increased, or if any entry has increased more than 1, enqueue the message
Accept the message

## Slide 15
A
B
C
Chat 1
Set<User>
Chat 1
Set<User>
Chat 1:
<empty>
Chat 1:
<empty>
Chat Creation (with network fault)
Resend queue:
B -> Create chat (chat 1)
Notes: Si perde il pacchetto di creazione chat

## Slide 16: Chat Creation (with network fault)
A
B
C
Chat 1:
<empty>
Chat 1:
<empty>
Resend queue:
B -> Create chat (chat 1)
Message 1
Chat 1
Message 1
Chat 1
Waiting for chat creation:
Message 1
Notes: C manda un messaggio, ma B non ha ancora ricevuto il pacchetto di creazione.
B tiene in attesa i messaggi fino all’arrivo del pacchetto di creazione.

## Slide 17: Chat Creation (with network fault)
A
B
C
Chat 1:
Message 1
Chat 1:
Message 1
Resend queue:
B -> Create chat (chat 1)
Chat 1
Set<User>
When the network recovers
All messages are received in correct order
Chat 1:
Message 1
Waiting for chat creation:
Message 1
Notes: Il pacchetto di creazione viene reinviato
Quando la connessione viene ristabilita, viene nuovamente inviato il pacchetto iniziale (contenente user e porta), che in questa slide è stato omesso.

## Slide 18: Peer’s disconnection
When a peer wants to leave the network, he will send to all his connected peers a ByePacket, informing them that he’s leaving.
Problem: how can a peer leave the network if he has messages to resend?
Create a new packet containing all the enqueued messages
Check and split this new packet into new ones according to the max UDP payload size
Send these packets to the discovery server
The peer disconnects
A
B
Discovery server
If the discovery server is unreachable, the peer can’t leave the network!

## Slide 19: Peer’s disconnection
A
B
Chat 1:
Message 1
Message 2
Resend queue:
B -> Message 1 (chat 1)
B -> Message 2 (chat 1)
B -> ByePacket
Discovery Server
Forwarding packet
Forwarding packet

## Slide 20: Peer’s disconnection
A
B
Chat 1:
Message 1
Message 2
Resend queue:
B -> Message 1 (chat 1)
B -> Message 2 (chat 1)
B -> ByePacket
Discovery Server
Forwarding packet

## Slide 21: Peer’s disconnection
B
Discovery Server
Chat 1:
Message 1
Message 2